## Slide 1: Hands on with FPGA’s: Module 6
Venkat Rangan

## Slide 2: Questions on Module 5
  Alarm clock

## Slide 3: Topics
Pre-class: Open floor for questions
  Module 5
Putting blocks together
  Busses
  NoC
  Protocols
FPGA Specifics
Open discussion

## Slide 4: Typical HW Design
Code up small blocks, target reuse
Interconnect blocks
Data path vs Control path
Image Processor
Pixels
Pixels
Done
Busy
Go
Num_rows
Num_cols
Other Params
Stats

## Slide 5: Busses
Common interface specification
  Fast design with fewer errors
Unidirectional data flow
Clearly defined accesses
  Single transactions
  Burst transactions
    More efficient than single xactions
    Well matched to external memories
E.g. Wishbone Specification, AXI, Avalon…

## Slide 6: The A in AXI, AHB, APB…
AMBA: ARM specification for on-chip interconnect

## Slide 7: Lets build a bus!
Use wb_intercon script
Actual blocks not implemented
CSR: Config, Status Registers
32 bits wide, good enough for most configuration type access
Camera
Processor
Encoder
RAM
CSR
0x60_0000 to
0x70_0000
0x00_0000 to
0x1F_FFFF
CSR
RAM
Wishbone 32
Empty

## Slide 8: NoC vs. Busses
Busses breakdown when there are many blocks
Hierarchy added to alleviate but adds delay
Network-on-Chip used for higher bandwidths
  Highly scalable and easily reconfigurable
  FLIT, PHIT
https://www.design-reuse.com/articles/10496/a-comparison-of-network-on-chip-and-busses.html
Open Source NoC using AXI
https://ignitarium.com/network-on-chip-an-overview/
https://ignitarium.com/network-on-chip-an-overview/

## Slide 9: Data Path Interconnects
Data only
  Assumes data is valid at every clock cycle
Data + Valid
  Data bus is used only when valid is active
Data + valid + ready
  Can flow control back to source
  Most flexible and easily extensible
Can also use NoC
  Higher overhead but good for large chips

## Slide 10: Valid-Ready Protocol Adapted from https://inst.eecs.berkeley.edu/~cs150/Documents/Interfaces.pdf
HW Block A
Data
Valid
Ready
HW Block B
Rule1: Data transfer happens when both Valid and Ready are active
Rule 2: No valid teasing: Once valid, cannot take away valid till ready is high
Rule 3: Ready can tease

## Slide 11
Single Data Transfer
Multiple data transfer (100% throughput)
No Data Transfer

## Slide 12: FPGA Process
Select FPGA Part: Make sure of the right part number!
Allocate pins
Specify clock(s)
Specify detailed Input/Output constraints
Map
Route
Bitgen

## Slide 13: Open

## Slide 14: Module 6:
Challenge

## Slide 15: Open Discussion