## Slide 1: Hands on with FPGA’s: Module 8
Venkat Rangan

## Slide 2: Questions on Module 7
Example of an end-end vision project using an FPGA: autonomous drone landing
  Could this be modified for your use cases?

## Slide 3: Topics
Pre-class: Open floor for questions
  Module 7
Guest Lecture: Dave Shah
APIO, LiteX: River, HW Intern @ tinyVision.ai
Beyond Verilog:
  High Level Synthesis
  CHISEL
When to use FPGA’s?
Open discussion

## Slide 4: Architecture Exploration: A FIR filter
FIR filter is a common design in signal processing
Design variables:
  How many multipliers?
  What clock speed do we want?
  Design reuse:
    Extendability for # of taps
    Bitwidths
    Signed vs. unsigned
int fir_filter(int xn) {
static int h[5] = {1,2,3,2,1};
// delay line of time samples
static int xd[5] = {0,};
// filter output
int yn = 0;
// implementation of delay line
xd[4] = xd[3];
xd[3] = xd[2];
xd[2] = xd[1];
xd[1] = xd[0];
xd[0] = xn;
// convolve delay line by // filter coefficients
for(int i=0;i<5;i++)
yn += h[i]*xv[i];
return yn;
}

## Slide 5: HLS Tools
What is HLS
Why HLS?
  Use C/Python as a HDL
  Interface synthesis: map I/O to stream/register/SPI etc. automatically
  Architecture exploration
  Fast verification
Example: Streamlogic.io
  HLS based video processing example
  Hardware-as-code series

## Slide 6: Other HDL’s…
CHISEL: Commercial RISCv processors written using this HDL
  See Chipyard for a detailed project
  Concept of generators vs. instances
    Also somewhat applicable to plain RTL designs!!!
  FIR Filter generator example using Chisel
    Generate Verilog using:
      import chisel3.stage.{ChiselStage, ChiselGeneratorAnnotation}
      val verilogString = chisel3.stage.ChiselStage.emitVerilog(new FirFilter(4, Seq(0.U, -1.S, 2.U, 5.U)) )
      println(verilogString)
    Moving average 13 bit filter, 4 taps:
      new FirFilter(13, Seq(1.U, 1.U, 1.U, 1.U))
    Triangular, 8 bit filter, 5 taps:
      new FirFilter(8, Seq(1.U, 2.U, 3.U, 2.U, 1.U))
Many others out there!

## Slide 7: FPGA’s: when/where?
 | FPGA | Microcontroller | Comments
Ease of programming | Difficult: you’re starting here! | Easy for simple applications | Some problems lend themselves well to FPGA’s vs. micro and vice-versa
Cost | Low to very high | Usually low | Wide range here for FPGA’s!
Toolchains/IDE’s | Lagging… | Well developed | 
Flexibility/Parallelism | Very high | Limited | Micros are good enough until they aren’t 
Energy Efficiency | Depends | Depends | FPGA’s work well for compute intensive tasks, micros are good for going to sleep and doing work occasionally
Many other criteria possible, very application specific!
Be very aware of pros/cons of each when choosing solutions

## Slide 8: Module 8:
Challenge:
  Install Chisel and the Chipyard on your computer (Beware, chipyard can take a loong time!!!) and play with it.
  Install Amaranth and apply some of the concepts you learnt in the class. You may want to try something simple like a counter at first and then start to stitch up more complex things like a CPU.
  Get CFU Play installed on your machine and go through the accelerator design. You should now have enough background to start working with this complex project.

## Slide 9: Open Discussion