## Slide 1: Hands on with FPGA’s: Module 5
Venkat Rangan

## Slide 2: Questions on Module 4
  State Machines
  Traffic light problem

## Slide 3: Topics
Pre-class: Open floor for questions
  Module 4
Memories: ROM, RAM
  Memory hierarchies
Playing with Memories
Structural vs Behavioral coding styles
Open discussion

## Slide 4: Memory Hierarchy
Non-volatile: ROM
Volatile: RAM
  Registers: very fast, small
  Compact bank of registers (register arrays)
    Found in very few FPGA’s
  Look Up Table RAM
    Very small, fast RAM
  Block RAM
    Usually ~10’s of Kb
  Large RAM
    Usually ~100’s of kB
  Off Chip: SRAM/DRAM
    Large, slow, high energy (1000x!)
By ComputerMemoryHierarchy.png: User:Danlash at en.wikipedia.org - ComputerMemoryHierarchy.png, Public Domain, https://commons.wikimedia.org/w/index.php?curid=9439275
Cost/Speed
Size/Energy

## Slide 5: Memories: Read Only Memory
Store programs, data
Can range from a small look up table through a full program
Game cartridges
UV EEPROM

## Slide 6: RAM Access
Byte access: more flexibility
Variable access widths
Single Port RAM
  Single clock domain
  Can do a single write/read per clock cycle
Pseudo Dual Port RAM
  Independent read/write ports
  Can have independent clock domains
True Dual Port RAM
  Each port and read/write independently

## Slide 7: Memories in Digital HW: System Level decisions
What kind of memory to use?
  How fast?
  How much data?
How wide should it be?
  How much data to process?

## Slide 8: Playing with memories
Experiment # | MEMSZ | DWIDTH | Number and Type of Memory
1 | 4 | 4 | 
2 | 4 | 8 | 
3 | 1024 | 8 | 
4 | 1024 | 32 | 
Lattice Radiant/Synplicity for Synthesis
What happens as we increase memory size?

## Slide 9: Understanding an FPGA: Lattice iCE40UP)

## Slide 10: Coding Style
Structural coding
  Specific FPGA features
  Found in low level netlists
  Excellent for timing
  Brittle code
Behavioral code
  Easy to understand
  Requires logic synthesis
  Sometimes have to use for IO cells, specialized blocks
module structural (
input logic a,
input logic b,
output logic y
);
and a1 (y,a,b); // AND gate instantiation
endmodule
module behavioral (
input logic a,
input logic b,
output logic y
);
assign y = a & b; // Behavioral description
endmodule

## Slide 11: Module 5: Memories
Challenge
  Code up a digital clock

## Slide 12: Open Discussion